## Slide 1
Recovering 3D Vibration Modes from
Asynchronous Multi-View Videos
A Gaussian-splat representation connects independently recorded image-space vibrations to shared spatial 3D mode shapes.
Goal. Use one mobile phone to scan a static scene and then record vibration from several fixed viewpoints at different times. Recover a view-consistent, high-detail 3D Gaussian model and spatial vibration fields without synchronized cameras.
End-to-end pipeline
1. Sweep + fixed videos
2. Joint COLMAP
3. Static 3DGS
4. Flow + Fourier modes
5. Pixel–Gaussian topology
6. View phase sync
7. Local 3D solve
8. Motion fill
Output: completed complex spatial fields φₖ ∈ ℂᴳˣ³
1. 3D Gaussian Splatting
3D Gaussian Splatting in one paragraph
3D Gaussian Splatting (3DGS) represents a scene as explicit, oriented, semi-transparent ellipsoids rather than a dense voxel grid (Kerbl et al., 2023). Each Gaussian stores
𝒢_g = (μ_g, Σ_g, o_g, c_g)
where μ_g ∈ ℝ³ is its center, Σ_g its 3D covariance, o_g opacity, and c_g appearance. A calibrated camera projects each Gaussian to an image-space ellipse. Depth-ordered alpha compositing gives
Ĉ(p) = Σᵢ Tₚ,ᵢ aₚ,ᵢ cᵢ, Tₚ,ᵢ = Πⱼ<ᵢ (1 − aₚ,ⱼ)
camera image
explicit centers support a 3D displacement field
2. Why Modal Analysis?
Pixels are too many degrees of freedom
Tracking P pixels independently produces a coupled displacement vector d(t) ∈ ℝ²ᴾ. Modal analysis replaces these dense degrees of freedom with a compact basis:
d(t) ≈ Φq(t) = Σₖ₌₁ᴷ φₖqₖ(t), K ≪ 2P
Each φₖ is a coherent spatial motion pattern and qₖ(t) is its temporal activation. Under small linear motion, modal coordinates approximately decouple. Only a few modes dominate the visible response: they are resonantly excited, lightly damped, and clearly projected into the camera.
m₁
m₂
two coupled degrees of freedom
Mode 1: in phase → → φ₁ ∝ [1, 1]ᵀ
Mode 2: out of phase → ← φ₂ ∝ [1, −1]ᵀ
Why the frequency domain?
Time-domain pixel motion mixes many modes. Because each mode has a natural frequency, the temporal Fourier transform separates their responses:
d̂(f) = Σₜ d(t)e⁻ⁱ²πᶠᵗ, d̂(fₖ) ∝ φₖ²ᴰ
Near a resonant peak fₖ, one spatial mode often dominates. Davis, Chen, and Durand recover projected complex 2D modes from ordinary video without geometry or material parameters:
fixed-camera
video
small optical
flow
temporal
FFT
resonant
peak
complex
2D mode
Each frequency slice is a candidate spatial pattern. Strong resonant peaks identify representative modes; their complex values retain displacement magnitude and relative phase.
Figure placeholder
bush_flow_and_frequency.png
Bush fixed-view optical flow, power spectrum, and one selected complex 2D mode.
Working assumptions
Small linear motion
Mode superposition and linear projection are valid.
Weak perspective
Small 3D displacement projects approximately linearly.
Well-spaced modes
One mode dominates near each resonant peak.
Broad-spectrum forcing
Relevant modes receive measurable excitation.
3. Why asynchronous multi-view is different
Synchronized camera arrays can triangulate the same moving surface at the same instant. Most users own one phone: they revisit viewpoints, but recordings start at different times and experience different forcing.
video 1
unknown start τ₁
video 2
unknown start τ₂
video 3
unknown start τ₃
same
object
same resonant frequency fₖ
different complex phase/gain
Time-domain optical flow from these recordings is not synchronized and should not match frame by frame. Our central modeling assumption is weaker:
Frequency-domain consistency assumption. If geometry, boundary conditions, and material properties remain fixed, the same natural frequency represents the same underlying 3D spatial mode. Each view may observe a different complex phase and amplitude.
Additional assumptions introduced by our setting
• A static sweep defines one canonical rest geometry.
• Fixed reference cameras are calibrated into that coordinate system.
• Vibrations remain small enough for camera and modal linearization.
• The same modes are excited across takes, although forcing strength and phase may differ.
• Frequencies are stable and sufficiently separated over the capture.
4. Solving shared 3D modes
A. Shared canonical scene
We sample a sweep video and add one reference image from each fixed view to the same COLMAP reconstruction. Registered sweep views train a foreground/background 3DGS; fixed cameras are exported for modal projection.
Figure placeholder
bush_capture_and_cameras.png
Sweep frames, fixed references, and registered cameras around the canonical scene.
B. Frequency evidence and observation topology
Foreground optical flow is transformed over time:
d̂ᵥ,ₚ(f) = Σₜ dᵥ,ₚ(t)e⁻ⁱ²πᶠᵗ
Greedy frequency selection chooses a compact set that reconstructs the observed flow spectra. Rendered depth unprojects each retained pixel to a canonical point Xᵥ,ₚ. Nearby Gaussians are ranked by
sᵥ,ₚ,₍g₎ = o_g exp[−½(Xᵥ,ₚ−μ_g)ᵀΣ_g⁻¹(Xᵥ,ₚ−μ_g)]
This creates a mode-independent observation topology connecting complex 2D measurements to plausible foreground Gaussian centers.
C. Synchronizing phase without synchronized time
At frequency k, view v observes a complex 2D displacement d̂ᵥ,ₖ,ₚ. For a Gaussian point g with complex 3D mode vector φₖ,g, first-order camera projection gives
d̂ᵥ,ₖ,ₚ ≈ αᵥ,ₖ Jᵥ,g φₖ,g
Jᵥ,g ∈ ℝ²ˣ³ is the camera projection Jacobian and αᵥ,ₖ ∈ ℂ is the unknown view-specific phase/gain.
Direct optimization of both φ and every α is bilinear. We set βᵥ,ₖ = αᵥ,ₖ⁻¹ and use points observed by multiple cameras. For one shared Gaussian:
A_g φₖ,g = B_g βₖ
C. Synchronizing phase (continued)
The columns of B_g place each view's measured complex flow in the corresponding view block. Let N_g span the left null space of the stacked Jacobian A_g:
N_gᴴ A_g = 0
Any set of view offsets explained by one common 3D displacement must therefore satisfy
N_gᴴ B_g βₖ = 0
shared Gaussian
multi-view J and d̂
SVD of stacked A_g
left-null N_g
aggregate N_gᴴB_g
across points
fix β₁,k = 1
solve remaining views
We aggregate these constraints over shared points, fix one reference-view gauge β₁,ₖ = 1, and solve a robust least-squares synchronization. Rank and information tests exclude views whose phase is not identifiable from the shared geometry.
Interpretation. The left-null projection removes the unknown 3D vector from synchronization. It asks only whether differently phased 2D observations could have come from some common 3D motion.
D. Spatial structure, local solve, and completion
Mutual KNN edges are removed across strong Gaussian-color or rendered-depth discontinuities. Remaining connected neighborhoods provide local structure. For a local first-order rigid component c:
φₖ,g = B_c,g ξₖ,c
The complex twist is obtained by matching its projections to all aligned 2D observations:
ξ*ₖ,c = arg min_ξ Σ₍ᵥ,ₚ,g₎∈𝒪_c w̄ᵥ,ₚ,g ‖αᵥ,ₖJᵥ,gB_c,gξ − d̂ᵥ,ₖ,ₚ‖₂²
A separate foreground graph propagates trusted observed motion into compatible unobserved Gaussians while preserving the measured solution.
Figure placeholder
bush_rigid_components.png
Bush Gaussian graph colored by local component or observation support.
Figure placeholder
bush_modes_grid.png
Representative completed Bush spatial 3D modes, shown from a common view and scale.
Current interpretation. The output modes are evidence-driven, spatially coherent complex displacement patterns. They are not yet mass- and stiffness-normalized structural eigenmodes. Accuracy depends on camera calibration, masks, optical flow, static Gaussian quality, and the shared-frequency assumption.
Notes: [Sources]
- docs/poster_drafts/bush_spatial_modes_poster_v2.tex (poster copy and layout source)
- C:/Users/zitengsong/Documents/school/research/dynamicGSPaper/Shape of Motion.pdf (3D Gaussian motion context)
- C:/Users/zitengsong/Documents/school/research/ISMB_Davis_2015.pdf (video modal analysis)
- Kerbl et al., 3D Gaussian Splatting for Real-Time Radiance Field Rendering, 2023.
[/Sources]