## Slide 1
Recovering 3D Vibration Modes from Multi-View Videos
with Gaussian Splatting
One sweep video builds the scene. Fixed cameras observe vibration. A shared 3D Gaussian representation lifts selected image-space frequencies into spatial 3D motion fields.
→
→
→
→
→
1
Sweep + fixed views
shared cameras
2
Static 3DGS
explicit 3D support
3
Dense optical flow
image motion
4
Frequency selection
complex 2D evidence
5
Local 3D solve
projected SE(3)
6
Motion fill
complete φₖ
INPUT
STATIC SCENE
VIBRATION EVIDENCE
SPATIAL 3D MODES
1
Why the problem is 3D
Dense optical flow tells us how pixels move, but not which 3D points moved or in what direction. A single image-space displacement can be explained by many 3D motions, so every camera must be expressed in one coordinate system.
IMAGE PLACEHOLDER
Sweep reconstruction + fixed cameras
bush_capture_and_cameras.png
→
2
A shared static scene
We jointly run COLMAP on sweep frames and one reference image from each fixed camera. The registered sweep reconstructs the static scene; the reference images place all observation cameras in that same world frame.
IMAGE PLACEHOLDER
Static Bush 3D Gaussian model
bush_static_3dgs.png
colored translucent 3D ellipsoids
3D Gaussian Splatting represents the scene with colored, translucent 3D ellipsoids. Their centers provide explicit locations where we can attach 3D displacement vectors.
𝒢g = (μg, Σg, og, cg)
wp,i = Tp,i ap,i · C(p) = Σi wp,i ci
Each pixel blends depth-ordered Gaussian contributions through opacity and transmittance.
Key representation choice
The geometry is neither a mesh nor a pixel grid. It is a set of explicit Gaussian centers μg with renderable appearance and learned shape. We solve motion directly at these centers and preserve the original static rendering model.
3
From video to frequency evidence
For each fixed view, dense optical flow gives a displacement trace dp(t) at every foreground pixel. A temporal Fourier transform converts that trace into complex motion evidence at frequency f: magnitude captures strength and phase captures timing.
d̂p(f) = Σt dp(t) e−i2πft
IMAGE PLACEHOLDER
Optical-flow spectrum and selected peaks
bush_flow_and_frequency.png
selected fₖ
Frequency selection is shared across views: we greedily choose a compact set whose reconstructed spectra explain the observed flow energy, then export the complex 2D mode at each selected frequency.
4
Pixel ↔ Gaussian topology
Following motion-aware Gaussian topology construction, each masked pixel is unprojected with the static depth map. Nearby Gaussian candidates are found in 3D, then ranked by an anisotropic Gaussian score rather than Euclidean distance alone:
sp,g = og exp[−½(Xp−μg)ᵀ Σg⁻¹ (Xp−μg)]
One pixel selects a small set of plausible 3D contributors
p
g1
g2
g3
high score
lower score
Across views, these correspondences form an observation topology 𝒪. It tells the solver which Gaussian centers are supported by which image-space mode samples; it is not yet a motion model.
Complex evidence matters
The real and imaginary parts are solved together. This retains relative phase between locations and cameras, which is essential for distinguishing spatial vibration patterns that share similar amplitude.
5
Local 3D motion solve
KNN edges are pruned across strong Gaussian-color and depth discontinuities. Remaining connected neighborhoods act as local components. For each frequency k, one complex SE(3) twist ξk,c produces a locally coherent displacement field:
φk,g = Bc,g ξk,c
IMAGE PLACEHOLDER
Color/depth-filtered local components
bush_rigid_components.png
The 3D field is solved by projecting candidate component motion into each camera and matching the complex 2D Fourier displacement:
ξ*k,c = arg minξ Σ(v,p,g)∈𝒪c w̄v,p,g ‖αv,k Jv,g Bc,g ξ − d̂v,k,p‖²
J projects a small 3D Gaussian displacement into image-space (u,v) motion.
6
Complete the field
Only Gaussians with reliable image observations receive a direct estimate. A separate foreground KNN graph propagates the solved motion into compatible unobserved Gaussians while preserving observed values.
IMAGE PLACEHOLDER
Motion fill across foreground Gaussians
bush_motion_fill.png
observed
filled by graph propagation
7
Bush spatial 3D modes
IMAGE PLACEHOLDER
Completed mode shapes at selected frequencies
bush_modes_grid.png
mode 1
mode 2
mode 3
mode 4
mode 5
mode 6
TAKEAWAY
1
One geometry
Joint COLMAP + static 3DGS puts every view in one 3D frame.
2
One evidence space
Complex optical-flow spectra preserve amplitude and relative phase.
3
One spatial output
The result is a completed complex displacement field φₖ ∈ ℂG×3.
Interpretation: these are evidence-driven spatial vibration patterns, not mass- and stiffness-normalized structural eigenmodes.
Notes: [Sources]
- Local project brief: docs/poster_brief/shape_of_motion_poster_brief.tex
- Local poster copy and layout: docs/poster_package/bush_internal_v1/poster_copy.md; docs/poster_package/bush_internal_v1/poster_layout.md
- Kerbl et al., “3D Gaussian Splatting for Real-Time Radiance Field Rendering,” ACM TOG 2023. https://doi.org/10.1145/3592433
- Schönberger and Frahm, “Structure-from-Motion Revisited,” CVPR 2016. https://doi.org/10.1109/CVPR.2016.445
- Farnebäck, “Two-Frame Motion Estimation Based on Polynomial Expansion,” SCIA 2003. https://doi.org/10.1007/3-540-45103-X_50
- Guo et al., “Motion-aware 3D Gaussian Splatting for Efficient Dynamic Scene Reconstruction,” arXiv:2403.11447. https://arxiv.org/abs/2403.11447
[/Sources]